## Slide 1: nebula @ BITS team bob

## Slide 2: agenda
Project Overview
The Packet
  Structure
  Assembly & Disassembly
Router Microarchitecture
  Router Overview
  Pipeline Stages
  VC Allocation FSM
  Routing Algorithms
Credit Based Flow Control & Arbitration
  Credit-Based Flow Control
  Arbitration Mechanism
Q & A

## Slide 3: Project Overview

## Slide 4: High level explanation
Output: A scalable NOC design for multi-GPU system
Topology: 2D mesh, 2x2 to 8x8 grid (up to 64 GPUs)
Protocols: ARM AMBA AXI4 (non-coherent), CHI (coherent)
Languages Used: SystemVerilog (RTL), Python (Analysis)
Key Features:
  Five-Stage Router Pipeline
  Adaptive and Deterministic Routing
  Credit Based Flow and Arbitration

## Slide 5: The Packet

## Slide 6: Packet Structure
Packets are decomposed into FLITs
  48-bit Header
  208-bit body
May be single- or multi-flit based on size
Routers are configured to handle QoS for prioritization

## Slide 7: Assembly and disassembly
Converts coordinates and metadata into predefined packets.
Payload segmentation splits large payloads across multiple flits to optimize transmission.
Ensures proper packet conversion for both AXI4 and CHI protocols.

## Slide 8: Router microarchitecture

## Slide 9: Router overview
Five-stage pipeline to process packets:
        Buffer Write
        Route Computation
        Virtual Channel Allocation
        Switch Allocation
        Switch Traversal
5 ports per router, 4 VCs per port
Four-stage FSM for VC control

## Slide 10: Router pipeline
Buffer Write
Route Computation
Virtual Channel Allocation
Switch Allocation
Switch Traversal

## Slide 11: Virtual Channel FSM
Idle
Routing
Waiting VC
Active
Notes: Each virtual channel maintains independent state, enabling concurrent packet processing across flows.
Transitions are driven by pipeline events: head/single flit arrival, route computation results, VC allocation success, and tail/single flit detection.
Coordination relies on switch arbitration signals for FIFO timing

## Slide 12: Navigating Q&A sessions
Maintaining composure during the Q&A session is essential for projecting confidence and authority. Consider the following tips for staying composed:
Stay calm
Actively listen
Pause and reflect
Maintain eye contact
Know your material in advance
Anticipate common questions
Rehearse your responses

## Slide 13: Speaking impact
Your ability to communicate effectively will leave a lasting impact on your audience
Effectively communicating involves not only delivering a message but also resonating with the experiences, values, and emotions of those listening

## Slide 14: Dynamic delivery
Learn to infuse energy into your delivery to leave a lasting impression
One of the goals of effective communication is to motivate your audience
Metric | Measurement | Target | Actual
Audience attendance | # of attendees | 150 | 120
Engagement duration | Minutes | 60 | 75
Q&A interaction | # of questions | 10 | 15
Positive feedback | Percentage (%) | 90 | 95
Rate of information retention | Percentage (%) | 80 | 85

## Slide 15: Final tips & takeaways
Consistent rehearsal
  Strengthen your familiarity
Refine delivery style
  Pacing, tone, and emphasis
Timing and transitions
  Aim for seamless, professional delivery
Practice audience
  Enlist colleagues to listen & provide feedback
Seek feedback
Reflect on performance
Explore new techniques
Set personal goals
Iterate and adapt

## Slide 16: Speaking engagement metrics
Impact factor | Measurement | Target | Achieved
Audience interaction | Percentage (%) | 85 | 88
Knowledge retention | Percentage (%) | 75 | 80
Post-presentation surveys | Average rating | 4.2 | 4.5
Referral rate | Percentage (%) | 10 | 12
Collaboration opportunities | # of opportunities | 8 | 10

## Slide 17: Thank you
Brita Tamm
502-555-0152
brita@firstupconsultants.com
www.firstupconsultants.com